## Slide 1
Sequencer board MKII : GS / Freedom electronics design
Has the SWO trace signal been brought out to the debug header?
See you tube phil’s lab

## Slide 2
Sequencer MkII
Firmware: SeqMk2PcbTest

## Slide 3
Serial port command record

## Slide 4
RCC (Reset & Clock Control) configuration
HSE Missing
8MHz – too high hence not installed
40MHz
40MHz
/1
40MHz
40MHz
40MHz
40MHz
Multispeed internal RC based clock
High speed internal RC based clock
/2,x10, /2
/1
RCC_MCO: Master clock output
PA8
/16
2.5MHz

## Slide 5
STM32L476VCT6
RCC_MCO
400ns period = 2.5MHz

## Slide 6
TIM1 configuration
40MHz
1000
40kHz
999
40Hz

## Slide 7
40MHz
Prescsaler
Timer 1
/39
CK-CNT
1MHz
Reload
RST
999
Update event
1kHz

## Slide 8
PD0: HSD1
RCC_MCO
DAC1
DAC2
CAN_TX
CAN_RX

## Slide 9
DAC voltage reference
-Vref needs to be tied to AVss
DAC
AVdd
AVss
+Vref
-Vref
DAC
AVdd
AVss
+Vref
-Vref
2.048 or 2.5V bandgap reference
+Vref pin is an input!
+Vref pin is an output!
To ADC Vref

## Slide 10
UART interface
FT234XD-R
5V
USB
Fuse removed

## Slide 11
To do:
Link +Vref to Avdd
Link –Vref to Avss
Remove USB fuse
Is USB 5V linked to general 5v supply on board?
To do:
Link +Vref to Avdd
Link –Vref to Avss
Remove USB fuse
Is USB 5V linked to general 5v supply on board?
Are keyswitch inputs 5V tolerant?
Power for I2C bus expander (MCP23017)? – 5V but not shown on circuit diagram along with C26
I2C pullup resistors? On both busses?
I2C device memory & port expander are on separate buses!
CAN connector on flying lead
Analogue outputs saturate with only a fraction of DAC output swing
Fuse removed from USB power supply – plug a USB cable in and we get an ‘unrecognised device’ error
FTDI device configuration?
Dummy loads for HS & LS drive
RS485 comms interface & cabling

## Slide 12
Which GPIO are 5V tolerant?

## Slide 13
MAX485 comms
Tx
Rx
Sequencer connection
B
A
Z
Y
Is silk screen incorrect?
PC4
USART3
PC5

## Slide 14
CAN1_Rx PB8
CAN1_Tx PB9
CAN interface
1Mbit/sec

## Slide 15
CAN interrupts:
HAL_CAN_Activation(CAN_HandleTypeDef * hcan, uint32_t ActiveITs)
Why would you use the macro???
To enable interrupts:
__HAL_CAN_ENABLE_IT(Handle, INTERRUPT)
__HAL_CAN_ENABLE_IT(&hcan1, CAN_IT_RX_FIFO0_FULL | CAN_IT_ERROR);
CAN_IT_RX_FIFO0_MSG_PENDING | CAN_IT_ERROR

## Slide 16
CAN setup

## Slide 17
CAN setup
Why have I still got this???

## Slide 18
MCP2551 (U5) p4:
CANRx Input to uC PB8: 10k series resistor too strong!!!
TTL CAN data output from PCAN & MCP2551
10k seems to be OK on the RS485 driver

## Slide 19
CAN issue on P1399 EOL test setup:
CAN transceiver wasn’t being enabled
Sequencer 2:
High value series resistors seem to be distorting original CAN pulses
PCAN seemed to stop working with the hardware!!!! Unplug and restart app got it working again!

## Slide 20
CAN TX issue on Sequencer MkII board 17APR2024
CAN Tx mailbox is successfully filled,
HAL_CAN_AddTxMessage() successfully called but no bitstream from the controller
Sending a message from PCAN seems to result in ‘bus heavy’ and single transmission turns into repeated PCAN transmission
The controllers CAN Tx line seems to produce error frames? (~41usec low pulses)
41/12 = 13.6usec/bit = 292kbit
Transmit priority?
CAN_TSR register reports: 0x1900 0008
CAN_ESR register reports 0x0700 0055
LEC[2:0] = 101 = Last error code = Bit dominant error
BOFF = 1
GF = 1
REC[7:0] = 0x07 = receive error counter
Controller was set to loop back mode & not physically connected to a CAN bus
TERR = 1

## Slide 21
18APR2024
CAN TX & RX series resistors bypassed – no improvement
PCAN CAN signal is reaching controller PB8
No hint of signal from PB9??? (CAN_Tx = PB9 = currently high (3.3V))
When processor is reset, the CAN_TX line jumps up to 5V
Remove R1 – break link with MCP2551. During processor reset this line now drops to 0V
Is the clock speed an issue?
CAN_BTR = 0x4010 0009
LBKM: Loopback mode enabled
SJW[1:0] = 0x01
BRP[7:0] = 0x09

## Slide 22
18APR2024 (2)
Try loopback in silent mode
Same error occurs – is there a problem with the chip?
Are PB8 & 9 5V tolerant? YES
Check clock configuration!!!!

## Slide 23
Pre 18APR2024 clock config
This doesn’t work!
This does work!
❶
❸

## Slide 24
This got the CAN working
Changed this and CAN loopback immediately started working!
This does work!
❷

## Slide 25
void HAL_CAN_RxFifo0MsgPendingCallback()
HAL_CAN_GetRxMessage()
HAL_CAN_ActivateNotification(&hcan1, CAN_IT_RX_FIFO0_MSG_PENDING)
CAN message reception
CAN message reception

## Slide 26
MISRA rules: place a ‘u’ after an unsigned int value

## Slide 27
I2C comms with external memory device
SDA
SCL
uC
PB13
PB14
I2C port 2
Uses Tx & Rx interrupts to prevent ‘blocking’
19APR2024
Wrong 16bit internal address seems to be sent

## Slide 28
Passing structures from functions
struct I2cConfig{
uint16_t I2cInternalAddress;
uint16_t I2cQuantity;
uint8_t I2cInternalAddressWidth;
uint8_t I2cDeviceAddress;
}structI2cConfig;
struct I2cConfig* GetI2cConfig(void)
{
return &structI2cConfig;
}
Function returns a pointer to the structure
GcI2cV1.c
main.c
#include "GcI2cV1.h“
struct I2cConfig* structptr;
structptr = GetI2cConfig();
Uint8_t x = structptr->I2cDevbiceAddress
Create a suitable pointer to the structure type
Pointer points to the data structure
GcI2cV1.h
This needs to be inm the h file to allow an instance to be made in main.c!!!

## Slide 29
RxBuffer1[0]
Single element buffer
RxBuffer2
RxWritePtr
Length: RXBUFFERLENGTH
RxBufferCount
RxReadPtr
RxString
RxStringLen
UART Receive interrupt
If Escape character is detected:
RxState | 0x08
If ‘delete’ character (\b) is detected, then
Decrement RxWritePtr & RxBufferCount

## Slide 30
XR function (Xmodem-CRC: 16bit CRC value)
❶ XR string detected
❷ Wait for delay to expire
❸ Wait for button to be pressed / timeout to expire
❹ Button pressed, waiting for x-modem data to arrive
❺ post button press timeout period expired
❻ EOT character detected (set by ISR), send ACK
❼ X-modem function terminated
❽ complete x-modem packet received (set by ISR), test CRC if failed, send NAK
❾ pull out individual line data from x-modem packet
❿ process line data (Process intel hex data)
11. send ACK
12 output intel hex data to destination device
133 BYTE PACKET
ACK
EOT(0x04)
C
Rx
Tx
ACK
Working single packet transfer
NAK

## Slide 31
133 BYTE PACKET
NAK
C
Rx
Tx
Single packet transfer with test error
132 BYTE PACKET??
Times out due to 132 bytes being received!!!

## Slide 32
Test key input
‘Mode1’ active high button has key attached: uC PB2: MODE1
MODE1_LED: current sink attached to PC8: MODE1_LED
MODE1_LED currently updated by TIM1 ISR at point of updating DAC output

## Slide 33
STM studio – separate software
Requires Java runtime environment (JRE)
Version 8 update 411 installed
Works through JTAG or SWD (Single Wire Debug)

## Slide 34
Import from an *.elf file…

## Slide 35
I2C setup
  I2C?: Query I2C settings
  I2CAx: Set number of address bytes
  I2CAxxxx: Set device internal address pointer
  I2CDxx: Set device address
I2C single byte read & write
I2C block read
XR:
  X modem packet reception